## Slide 1
BANGLADESH TECHNICAL EDUCATION BOARD
DIPLOMA IN ENGINEERING
POWER TECHNOLOGY
4 th semester
Lesson 01
Subject: IC Engine Details (27141)
Md. Naimur rahman
JUNIOR INSTRUCTOR
POWER TECHNOLOGY
Sylhet polytechnic institute, stlhet

## Slide 2
Dimension of IC engines

## Slide 3: POWER PRODUCING DEVICES
I.C. ENGINE
FOUR STROKE PETROL & DIESEL ENGINE TWO STROKE PETROL & DIESEL ENGINE
TURBINE
IMPULSE REACTION
BOILERS

## Slide 4: I.C. ENGINE
ENGINE
Mechanical device which converts one form of energy into another form
I.C. ENGINE
Engine in which combustion take place inside engine cylinder is called IC engine. E.g.-Aircraft engine, Automobile Engines

## Slide 5: I.C. ENGINE

## Slide 6: CLASSIFICATION OF I.C. ENGINE
















1. CYCLE OF OPERATION
Two stroke engine
Four stroke engine
  THERMODYNAMIC CYCLE
Otto cycle Diesel cycle Dual cycle
  METHOD OF IGNITION
S.I. ENGINE C,I. ENGINE
NO. OF CYLINDERS
Single Multi
COOLING SYSTEM
Air cooled Water cooled Oil cooled

## Slide 7: CLASSIFICATION OF I.C. ENGINE
FUEL USED
  Petrol
  Diesel
  Gas
SPEED
High speed Lows peed Medium speed
APPLICATION
Automotive engines Aircraft engines Marine application Generator sets

## Slide 8: CLASSIFICATION OF I.C. ENGINE
ARRANGEMENT OF CYLINDERS
  Vertical
  Horizantal
  V- engine
  Radial engine
  Opposed cylinder
  Opposed piston

## Slide 9: TERMINOLOGY
BORE
STROKE
TDC
BDC
CLEARENCE VOLUME
SWEPT VOLUME
COMPRESSION RATIO

## Slide 10: Components of Four-Stroke Engines
Intake Valve
Valve Cover
Intake Port
Head
Coolant
Engine Block
Oil Pan
Oil Sump
Crankshaft
Camshaft
Exhaust Valve
Spark Plug
Exhaust Port
Piston
Connecting Rod
Rod Bearings
Back
Next
Diagram

## Slide 11: Four Stroke Cycle
10
Intake
Compression
Power
Exhaust

## Slide 12: Intake Stroke
11
Intake valve opens.
Piston moves down, ½ turn of crankshaft.
A vacuum is created in the cylinder.
Atmospheric
pressure
the air/fuel
into the
pushes mixture cylinder.

## Slide 13: Compression Stroke
12
Valves close.
Piston moves up, ½ turn of crankshaft.
Air/fuel mixture is compressed.
Fuel starts to vaporize and heat begins to build.

## Slide 14: Power Stroke
13
Valves remain closed.
Spark plug fires igniting fuel mixture.
Piston moves down, ½ turn of crankshaft.
Heat is converted to mechanical energy.

## Slide 15: Exhaust Stroke
14
Exhaust valve opens.
Piston move up, crankshaft makes ½ turn.
Exhaust gases are pushed out polluting the atmosphere.

## Slide 16: Four Stroke Cycle Animation
15

## Slide 17: TWO STROKE ENGINE

## Slide 18: Two Stroke Animation
17

## Slide 19: Diesel Animation
18

## Slide 20: PETROL V/S DIESEL ENGINE
Diesel cycle
Only air sucked during suction stroke
No spark plug needed
C.R.= 14-22
High efficiency
Heavy
Costly
More
Trucks,buses,gensets
Otto cycle
Air – fuel mixture suction stroke
spark plug is needed
C.R.=6-12
Low efficiency
Light weight
Cheap
Less vibration & noise
Motor cycles, cars, light duty vehicles
PETROL ENGINE (S.I.)
DIESEL ENGINE(C.I.)

## Slide 21: TWO STROKES V/S
Cycle - 1 rev & 2 strokes
1 power stroke per Rev.
Ports
Simple ,light weight , low cost
More power for same size engine
Piston shape –crown
Less efficiency
E.g, mopeds, scooters
FOUR STROKES
Cycle-2rev & 4strokes
1 Power stroke per 2 Rev
valves
Complicated, heavy
, costly
Less power
Flat piston
More efficiency
Cars, bikes,trucks,buses
TWO STROKES
FOUR STROKES