## Slide 1
BANGLADESH TECHNICAL EDUCATION BOARD
DIPLOMA IN ENGINEERING
POWER TECHNOLOGY
4 th semester
Lesson 03
Subject: IC Engine Details (27141)
Md. Naimur rahman
JUNIOR INSTRUCTOR
POWER TECHNOLOGY
Sylhet polytechnic institute, stlhet

## Slide 2
Features of IC engines

## Slide 3
types of heat engines
external combustion
internal combustion
steam engines
turbines
Stirling engine
Otto engine
Diesel engine
Vankel engine
Internal Combustion Engines

## Slide 4
Internal Combustion Engines
The internal combustion engine is an engine in which the combustion of fuel-oxidizer mixture occurs in a confined space
applied in:
automotive
rail transportation
power generation
ships
aviation
garden appliances

## Slide 5
Internal Combustion Engines

## Slide 6
Internal Combustion Engines

## Slide 7
Internal Combustion Engines – Theorem Carnot cycle -
Carnot's theorem is a formal statement of this fact: No engine operating between two heat reservoirs can be more efficient than a Carnot engine operating between those same reservoirs.

## Slide 8
Internal Combustion Engines – Carnot cycle -
TH is the absolute of cold reservoir
TC is the absolute of hot reservoir

## Slide 9
Internal Combustion Engines – two stroke -
1. Power / Exhaust
ignition
piston moves downward compressing fuel-air mixture in the crankcase
exhaust port opens
2. Intake / Compression
inlet port opens
compressed fuel-air mixture rushes into the cylinder
piston upward movement provides further compression

## Slide 10
Internal Combustion Engines – two stroke -
Advantages:
lack of valves, which simplifies construction and lowers weight
fire once every revolution, which gives a significant power boost
can work in any orientation
good power to weight ratio
Drawbacks:
lack of a dedicated lubrication system makes the engine to wear faster.
necessity of oil addition into the fuel
low efficiency
produce a lot of pollution

## Slide 11
Internal Combustion Engines – four stroke -
starting position
a. piston starts moving down
b. intake valve opens
c. air-fuel mixture gets in
1. intake
a. piston moves up
b. both valves closed
c. air-fuel mixture gets compressed
2. compression

## Slide 12
Internal Combustion Engines – four stroke -
ignition
a. air-fuel mixture explodes driving the piston down
3. power
a. piston moves up
b. exhaust valve opens c. exhaust leaves the cylinder
4. exhaust

## Slide 13
Internal Combustion Engines – four stroke -
Advantages:
dedicated lubrication system makes to engine more wear resistant
better efficiency that 2-stroke engine
no oil in the fuel – less pollution
Drawbacks:
complicated constriction
should work in horizontal position due to lubrication

## Slide 14
Internal Combustion Engines – four stroke -
air intake
compression
fuel injection
combustion
exhaust
exhaust /intake

## Slide 15
Internal Combustion Engines – Diesel -
Advantages:
self ignition (without electrical spark plug)
better efficiency
reliability
higher durability
supplied with worse fuels
Drawbacks:
more expensive production
more weight
louder
lower revolutions

## Slide 16
Internal Combustion Engines – Diesel -

## Slide 17
Internal Combustion Engines – multi-cylinder -
Cylinder layouts

## Slide 18
Internal Combustion Engines – multi-cylinder -
Cylinder layouts
flat
inline
V TYPE

## Slide 19
Internal Combustion Engines – multi-cylinder -
inline
flat
„boxer”
V

## Slide 20
Internal Combustion Engines – multi-cylinder -
14 cylinder Diesel engine (80 MW)

## Slide 21
Internal Combustion Engines – multi-cylinder -
Cylinder layouts
radial

## Slide 22
Internal Combustion Engines
Valve operation

## Slide 23
Engine characteristic
Diesel
Petrol

## Slide 24
Internal Combustion Engines
Engine cooling

## Slide 25
Internal Combustion Engines
Turbocharged engine

## Slide 26
Internal Combustion Engines
Wankel rotary engine
Advantages:
higher power output
no reciprocating mass
simpler and lighter construction
Drawbacks:
increased wear of rubbing parts
higher fuel consumption
requirement for better materials

## Slide 27
THANK YOU